IRPNotation Version 3
Some ideas by Bengt Martensson 2014-07-29, 2015-09-20

General principles

Definition: A modulated IR sequence consists of a modulation frequency, an optional duty cycle (a number 0 < duty_cycle < 1), and an even number of durations, stating on- and off-times, the ones with even index (stating with 0) denoting on-times, the other off-times.

A non-modulated IR sequence is considered as having the modulation frequency 0.

An implementation may allow odd sequences by adding an implementation dependent off-time, e.g. 100ms.

On input to a program, if the numbers are given as signed, positive numbers are to be taken as on-times, the negative as off-times, whereby consecutive numbers of same sign are lumped together. Zeros (0) are semantically nonsensical, and are therefore explicitly forbidden.

Basic Objects: Replace parameter discussion by

Semantics of the parameters
In the context of the IRP notation, the parameters in a protocol a priori do not carry any semantics at all. By convention, when using the protocols, the following semantics has been established:

F = Function code (sometimes called OBC or Original Button Code, or command number)
D = Device code
S = Subdevice code
T = Toggle.

It is not required, however strongly recommended, that the “most frequently changing parameter” in a protocol is called “F”, the next one “D”, and so on. T should only be used for a signal having toggling semantic.

Overall structure: Adjust according to repetition syntax change, see below.
protocol = generalspec, bitspec, variation, [definitions] [parameterspec];
protocol = generalspec, bitspec, irstream, [definitions] [parameterspec];

The GeneralSpec section
Add duty cycle as an integer followed by “%”.

In the version 2 of the notation, implementing the GenaralSpec as described is very difficult, a difficulty that in no way reflects a real need. For the ease of implementation, e.g. fix the order of the entries can be fixed.
Duration
1. Extents
  Semantics: Add:
  Extents are only allowed as the final element of a bare_irstream. Thus the often used constuct (…., ^xxx,(....^yyyy)*) will be illegal, and should be rewritten as ((…., ^xxx),(....^yyyy)*) (There may be a compabiblity mode of a parser that interprets the former as the latter.)
2. Bitspecs
Remove the third parameter (is replaced by right shift operation). Prohibit leaving out the second operator (this was just used for implementing a shift operator anyhow.) Remove the leading ~ form (~ will be a unary operator instead)

IrStreams
1. Bitspecs
2. Repeat Markers
  prohibit the infinite repeat markers; this now has to be described by Variations.
3. Expressions
  new: ~ unary operator
  new: Shift operators, like C
  Logical operators, like in my description
  BitCount as per IrpMaster
  protocol-specific functions, see 20.
4. Definitions
5. Assignments
6. Variations
  Should be the only possibility to express intro, repeat, ending, Intro, repeat required, even if empty, ending optional. Intro- and ending sequences may be suffixed by a finite constant repeat marker, repeat by an infinite repeat marker, default *. All repeat sequences must be equal! (which prohibit assignments in repeats)
7. Names and numbers
  as per IrpMaster, first section (not second)
8. Execution model
replace by:

From an IRP-Protocol and a parameter assignment compatible with its parameter specification, it is the task of rendering program to compute three modulated IR-sequences, of which any one (but not all) may be empty: start- repeat-, and ending sequence. A non-empty ending sequence is only allowed together with a non-empty repeat sequence. Taking persistent variables into account, the rendered IR sequences are unique determined.

1. Parameter specification
  as per IrpMaster. Allow constant expressions therein? ([A:0..4294967295] is disgusting....)
2. Comments and line breaks
  as per IrpMaster
3. Data types
  as per IrpMaster
4. Multiple definitions
  as per IrpMaster
5. Inheritance
  as per IrpMaster
6. protocol specific functions
  For e.g. complicated computations, in particular checksums (CRCs). Either “linking in” native functions, or to have an embedded extension language.