IRPNotation Version 3
Some ideas by Bengt Martensson 2014-07-29, 2015-09-20, 2016-07-29

General principles

Definition: A modulated IR sequence consists of a modulation frequency, an optional duty cycle (a float number 0 < duty_cycle < 1), and an even number of durations, stating on- and off-times, the ones with even index (stating with 0) denoting on-times, the other off-times. (In particular, an IR sequence starts with a flash and ends with a gap.)

An implementation may allow odd sequences by adding an implementation dependent off-time, e.g. 100ms.

A non-modulated IR sequence is considered as having the modulation frequency 0.

On input to a program (an optionally on output), if the numbers are given as signed, positive numbers are to be taken as on-times, the negative as off-times, whereby consecutive numbers of same sign are lumped together. Zeros (0) are semantically nonsensical, and are therefore explicitly forbidden. An implementation may chose to “forgive” by just ignoring them.

Basic Objects: Replace parameter discussion by

Semantics of the parameters
In the context of the IRP notation, the parameters in a protocol a priori do not carry any semantics at all. By convention, when using the protocols, the following semantics has been established:

F = Function code (sometimes called OBC (for Original Button Code), or command number)
D = Device code
S = Subdevice code
T = Toggle (has memory (and default) in the sense of Parameter Specification, the IRP code “toggles” it between the allowed values, normally 0 and 1)

It is not required, however strongly recommended, that the “most frequently changing parameter” in a protocol is called “F”, the next one “D”, and so on. T should only be used for a signal having toggling semantic. This means that its value is persistently stored between invocations, cf. the @-form in the parameter spec.

Overall structure: Adjust according to repetition syntax change, see below.
protocol = generalspec, bitspec, variation, [definitions] [parameterspec];
protocol = generalspec, bitspec, irstream, [definitions] [parameterspec];

The GeneralSpec section
Add duty cycle as an integer followed by “%”.

In the version 2 of the notation, due to the use of exclusions, implementing the GeneralSpec as described is very difficult, a difficulty that in no way reflects a real need. For the ease of implementation, a left-to-right semantic (redundant entries accepted, parsed left to right, later entries overwrite earlier) is suggested.
Duration
Flashes and gaps/etxtents do not need to be interleaved. In this case, the implementation should lump several consecutive flashes (gaps/extensions) together, before delivering the rendered output.

Extents
Extents are only allowed as the final element of a bare_irstream. Thus the often used
constuct (...., ^xxx,(....^yyyy)*) will be illegal, and should be rewritten as ((...., ^xxx),
Syntax: note that while the specification implicitly seems to assume that there are only one extent in a bare_irsteam, and it occurs at the end of it, this is never explicitly required. Semantics: Change
“An extent has a scope which consists of a consecutive range of items that immediately precede the extent in the order of transmission in the signal. “
to
“An extent has a scope which consists of a consecutive range of items that immediately precede the extent in the order of transmission in the signal, starting with the first element after the last preceding extent, or from the start if there is no preceding extent.”
1. Bitspecs
Remove the third parameter (is replaced by right shift operation). Prohibit leaving out the second operator (this was just used for implementing a shift operator anyhow.) Remove the leading ~ form (~ will be a unary operator instead). (These changes would simply make the rules simpler, thus simplifying both the understanding for a human reader and the implementation in a program.)

IrStreams
Conditional IrStreams...
1. Bitspecs
2. Repeat Markers
  prohibit the infinite repeat markers; this now has to be described by Variations.
  The syntax and semantics of the repeats was obviously borrowed from regular expressins, and make little sense in the context of IR signals, where an intro-, a repeat-, and an ending sequence are required. The IRP allows for not only several infinite repeats, and even hierarchical repeats, which are concepts which do not make sense either in the context of a hardware “clicker”, nor as a program that can send an IR signal n times. IR Transmogrifier allows only one infinite repeat. It uses a state machine model to generate the intro-, repeat-, and ending sequences from the IRP form.
3. Expressions
  propose rename expression → para_expression; bare_expression → expression
  new: ~ unary operator
  new: Shift operators, like C
  Logical operators, like in my description
  BitCount as per IrpMaster
  protocol-specific functions, see 20.
4. Definitions
5. Assignments
6. Variations
  Should be the only possibility to express intro, repeat, ending, Intro, repeat required, even if
  empty, ending optional. Intro- and ending sequences may be suffixed by a finite constant
  repeat marker, repeat by an infinite repeat marker, default *. All repeat sequences must be
  equal! (which prohibit assignments in repeats)
  Syntax: Variation must appear only as part of an irstream with infinite repeat. The first and the last may be empty, but not the middle one.
  Semantic; The sequence
        (FOO, [I][R][E], BAR)+
should be equivalent to
(FOO, I, BAR, (FOO, R, BAR)*, FOO, E, BAR)
provided that all of I, R, and E are nonempty. If e.g. E is empty, then FOO, E, BAR disappears
Should be the only possibility to express intro, repeat, ending, Intro, repeat required, even if empty, ending optional. Intro- and ending sequences may be suffixed by a finite constant repeat marker, repeat by an infinite repeat marker, default *. All repeat sequences must be equal! (which prohibit assignments in repeats)
1. Names and numbers
  as per IrpMaster, first section (not second)
2. Execution model
replace by:

From an IRP-Protocol and a parameter assignment compatible with its parameter specification, it is the task of rendering program to compute three modulated IR-sequences, of which any one (but not all) may be empty: start- repeat-, and ending sequence. A non-empty ending sequence is only allowed together with a non-empty repeat sequence. An empty repeat signal seldomly makes sense, for example for an IR sending engine, but can be sensible in some situations, like waiting for a key press, and then waiting for a key release,

Taking persistent variables into account, the rendered IR sequences are unique determined.

1. Parameter specification
  as per IrpMaster. In particular, persistent variables should be added. Allow constant expressions therein? ([A:0..4294967295] is disgusting.…) (IrpTransmogrifier understands UINT8_MAX, UINT16_MAX, UINT24_MAX, UINT32_MAX, UINT48_MAX, 'UINT64_MAX).
2. Comments and line breaks
  as per IrpMaster. (Only the embedding of IRPs in (the primitive format) IrpProtocols.ini makes the escaping of the line endings necessary.)
3. Data types
  as per IrpMaster
4. Multiple definitions
  as per IrpMaster
5. Inheritance
  as per IrpMaster
6. protocol specific functions
  For e.g. complicated computations, in particular checksums (CRCs). Either “linking in” native functions, or to have an embedded extension language.